a)CLOCK THE GATE: Find the bus that your timer is connected (Hint all the timers are connected to either APB1 or APB2).
Find the relevant enable register in the RCC special function register and set it to 1.

#include "stm407xx.h"
RCC->APB1ENR |= RCC_APB1ENR_TIM2EN;
// open TIM2 clokk in APB1 way

b) INITIALIZE THE TIMER:
Each timer has more than 20 subregisters but luckily in order to use any of them as basic timer we only need to set 2 subregisters.
Set the prescaler register (psc is used for short) to 2.
Set the autoreload register to ARRNUMBER

TIM2->PSC = 999;
TIM2->ARR = 10000;

c) START THE TIMER:
in order to start a timer you have to set the control register of that timer to 1.In the data sheet and stm32f407xx.h file it is abbreviated as CR1.So set CR1 to 1 to start the timer and set CR1 to 0 to top it.

// Start
TIM2->CR1 |= TIM_CR1_CEN; // Set 1
// Stop
TIM2->CR1 &= ~TIM_CR1_CEN; // Set 0

D)WATCH THE COUNT VALUE: Whenever the timer starts hardware increments the count register of the timer (CNT for short) increments by 1 at every cycle of the MCU.You can read its value through CNT register.

uint32_t count = TIM2->CNT;

YOUR TASK: You will use the timer specified by your Timernumber to count up to Duration. Whenever it reaches the duration the timer should stop ,set the CNT register to 1,toggle the led specified by LEDPINNUMBER and start again (in main while loop).

##include "stm32f4xx.h"

#define LED_PIN 14

void init_timer() {
    RCC->APB1ENR |= RCC_APB1ENR_TIM12EN;
    TIM12->PSC = 0;
    TIM12->ARR = 65535;
    TIM12->CR1 |= TIM_CR1_CEN;
}

void init_led() {
    RCC->AHB1ENR |= RCC_AHB1ENR_GPIODEN;
    GPIOD->MODER |= (1 << (LED_PIN * 2));
    GPIOD->BSRR |= (1 << LED_PIN);
}

int main() {
    init_timer();
    init_led();

    while (1) {

        if (TIM12->CNT >= 31140) {
        GPIOD->BSRR |= (1 << (LED_PIN + 16)); // Turn on LED
        }

        if (TIM12->CNT >= 65535) {
        GPIOD->BSRR |= (1 << LED_PIN); // Turn off LED
        TIM12->CNT &= 1;
        }
    }
}

https://github.com/CrowMasyt/EE242-mid-led2